# Introduction
# SMSC Driver™ Software for Linux: Release Notes

### SMSC Driver for Linux
Software Package: xf86-video-smsc_1.0.2.1-20111206
Version: 1.0.2.1
Release Date: December 6, 2011
The SMSC Driver for Linux supports the use of SMSC UFX-6000 and UFX-7000 USB graphics controller devices in a linux environment. The driver supports the use of one or multiple devices with high-quality graphics and performance.
### Viewspan Graphical Configuration Tool
Software Package: viewspan_1.0.2.1
Version: 1.0.2.1
Release Date: December 6, 2011
Viewspan is a simple, graphical application to easily set up a dual-monitor system where one additional monitor is connected to an SMSC USB Graphics controller. With Viewspan, users can quickly and easily configure the position and behaviour of the SMSC-connected monitor without manually editing configuration files.
Please Note: Manual configuration is required if the user wishes to have more than one additional monitor.

# Features
SMSC Driver Software delivers the following features:
- X.Org-based driver for SMSC® UFX-6000/7000 USB Graphics Controller devices on Linux
- support for X.Org X server 1.7.6 and later.
- support for multiple devices when used with the Userful MultiSeat software package
- support for multiple devices under Xinerama with graphical or manual configuration
- hardware cursor accleration
- EXA support
The Viewspan application provides:
- simple, intuitive graphical interface for setting up a dual-monitor system, where one monitor is connected to the onboard GPU and the other is connected to an SMSC UFX device
- one-click controls for specifying:
  - which monitor (onboard or SMSC) is primary
  - display modes (extended desktop, cloned desktop, deactivated display)
  - position of the extended desktop (relative to the primary monitor's desktop)
  - VGA or HDMI video output from the SMSC-connected monitor
# Supported Operating Systems
The SMSC-Driver for Linux has been extensively tested and is supported on the following operating systems:
- Ubuntu 10.04 32-bit (Using version 1.7.6 of the X Server)
- Ubuntu 10.04 64-bit (Using version 1.7.6 of the X Server)
- RHEL-6/CentOS 6 32-bit (Using version 1.7.7 of the X Server)
- RHEL-6/CentOS 6 64-bit (Using version 1.7.7 of the X Server)
The driver is compatible with other versions of the X server from version 1.7.6 up to and including 1.10.1.
# PC Recommended Specifications
SMSC Driver Software can be used on a range of processors; the performance of the software is dependent upon the processing power available, and so more capable systems offer higher performance.
### For Stand-Alone Use
The Driver and Viewspan software is compatible with any video card supported by the underlying Linux distribution and it's included version of the X Server.
- Information on what video cards are supported by open-source linux drivers can be found in the X.Org Wiki (http://www.x.org/wiki/Projects/Drivers).
- Information on video cards supported by Ubuntu/Edubuntu 10.04 can be found in the Ubuntu documentation (https://help.ubuntu.com/10.04/installation-guide/i386/hardware-supported.html).
- For information on RHEL6, please refer to the Red Hat documentation (http://docs.redhat.com/docs/en-US/Red_Hat_Enterprise_Linux/6/).
### For Use in a MultiSeat Configuration
Recommended typical system/hardware requirements are:
For up to 6 stations:
- Dual Core Processor
- 2GB RAM
- 1 high-speed USB controller interface
For up to 11 stations:
- Quad Core Processor
- 4GB RAM
- 2 high-speed USB controller interfaces
If the PC specification is below this, performance will be lower (or CPU loading higher).

# Hardware
To use the driver in stand-alone mode, connect a monitor to the UFX device and then connect the device to a system USB port with a standard USB A-to-B cable.
Input devices (keyboard, mouse) may also be connected to the UFX board. These devices operate independently of the video chipset, and will be assigned to the computer system as if they were connected to a simple USB hub.
Audio devices connected to the UFX board will also operate as if on a simple USB hub (i.e./ regardless of what mode the video chipset is running in). In Linux systems, it is important to open “Sound Preferences” (by right-clicking on the “speaker” icon in the upper-right corner of the desktop) and choose the “PnP USB audio device” to use the UFX device for audio.
### Monitor Resolution
For best results, SMSC recommends using only monitors that support this resolution natively. In addition, if two or more monitors are configured in an Extended or Mirrored mode, for best results both monitors should be the same size and the same native resolution, or at least the same aspect ratio.
# Installation
### Driver
Save the SMSC linux driver package (xf86-video-smsc_[version]-[commit]_[arch]) to the desktop of the system. Then, either:
- double-click the package to launch the distro package manager, OR
- in a terminal, navigate to where the package is saved and enter:
For RHEL-6/CentOS-6 (as root):
$ rpm -i xf86-video-smsc_[version]-[commit]_[arch].rpm
For Ubuntu:
$ sudo dpkg -i xf86-video-smsc_[version]-[commit]_[arch].deb
### Viewspan
Save the Viewspan package (viewspan_[version]-[commit]_[arch]) to the desktop of the system. Then, either:
- double-click the package to launch the distro package manager, OR
- in a terminal, navigate to where the package is saved and enter:
For RHEL-6/CentOS-6 (as root):
$ rpm -i viewspan_[version]-[commit]_[arch].rpm
For Ubuntu:
$ sudo dpkg -i viewspan_[version]-[commit]_[arch].deb
# How to Use
The SMSC Driver for Linux is designed to work either as a stand-alone video driver or in conjunction with Userful MultiSeat™ software. Guidelines for each use case are below.
### Stand-Alone Driver
The "stand-alone" driver can be used with one or as many as 10 extra monitors in extended or cloned configurations using the X server extension called Xinerama.
#### With Viewspan for One Extra Monitor
The SMSC Driver for Linux supports the use of an extra monitor to achieve a dual-monitor setup, and the Viewspan application allows a user to easily configure the dual-monitor setup without the need to edit configuration files manually.
##### Launching the ViewSpan Application
The Viewpsan application opens automatically whenever a UFX-6000 SMSC chipset device is connected to the system. This behavior can be changed by un-checking the "Auto launch ViewSpan when SMSC detected" option in the ViewSpan interface.
A user can also launch Viewspan from the desktop panel menus (see image at right): Applications > System Tools > SMSC ViewSpan.

##### Configuration Options
The Viewspan application lets the user configure the dual-monitor system by choosing from the following options:
1. Choose primary display. Specify whether the onboard GPU or the SMSC GPU is to be designated as the primary display. This can impact performance and behavior since many programs with graphical elements (including but not limited to video players) automatically select output modes based on the capabilities of the primary GPU.
2. Choose output of SMSC. For SMSC devices that have an HDMI output port, this option allows it to be used.
3. Choose behavior of secondary display. Choose between "Extended desktop", "Mirrored desktop", or "Deactivate display".
4. Choose extended secondary monitor position. If the chosen display mode is "Extended desktop", specify the physical position of the secondary monitor.
5. Auto launch ViewSpan when SMSC detected. If this box is checked, Viewspan will launch whenever a UFX-6000 SMSC chipset device is connected to the system.

##### How Does Viewspan Work?
Essentially, Viewspan allows a user to select configuration options (such as display mode, output, and spatial position) that are then written to a configuration file, /etc/X11/xorg.conf.
It is important to note that each time Viewspan is used to set up or change configuration of the dual-monitor system, the xorg.conf file is overwritten with a newly generated configuration file. This means that any manual changes made to the xorg.conf file are lost whenever Viewspan is used. To close the Viewspan application without writing a configuration file, be sure to click on the Cancel button.
For reference, a sample xorg.conf file is below. This system was using an nVIDIA graphics processor with the "nouveau" driver.
The Viewspan Configuration was (as seen in the image of the application interface above):
- onboard GPU as primary display
- VGA output on the SMSC device
- Extended desktop
- extended secondary monitor in the right position.
Section "Files"
        ModulePath "/usr/lib/nvidia-current"
        ModulePath "/usr/local/lib/xorg/modules"
        ModulePath "/usr/lib/xorg/modules"
        ModulePath "/usr/lib64/xorg/modules"
        ModulePath "/usr/lib/userful/xorg/modules"
EndSection

Section "Device"
        Identifier "OnboardCard"
        Driver "nouveau"
        VendorName "nVidia"
        BoardName "nVidia card"
EndSection

Section "Device"
        Identifier "SMSCCard"
        Driver "smsc"
        Option "Device" "usb-0000:00:1d.0-1.3.1"
        Option "SGFX" "GfxPort=VGA"
EndSection

Section "Screen"
        Identifier "OnboardScreen"
        Device "OnboardCard"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "Screen"
        Identifier "SMSCScreen"
        Device "SMSCCard"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection
Section "ServerLayout"
    Identifier "Extended"
    Screen 0 "OnboardScreen"
    Screen 1 "SMSCScreen" RightOf "OnboardScreen"
    Option "Xinerama" "on"
    Option "IgnoreABI" "True"
EndSection
#### Manual Configuration for 2-10 Extra Monitors
The SMSC Driver for Linux supports the use of up to 10 additional monitors using Xinerama. To achieve these more complex configurations, a user must manually edit the /etc/X11/xorg.conf file.
##### Basic Guidelines
To successfully extend or mirror the primary desktop over more than one extra monitor, the following sections of the xorg.conf file must be adjusted to fit the desired hardware to be used. For reference, please see the examples below.
1. Section "Device"
  1. There must be one "Device" section for each GPU. This means one for the "OnboardCard" and one for each SMSC device-connected monitor.
  2. The "OnboardCard" Device section must specify the Driver that the onboard graphics processor is using. The common open-source drivers are listed below; if using a proprietary driver, that driver must be listed in this section.
    1. nVidia cards commonly use the open-source drivers "nouveau" or "nv"
    2. ATI cards typically use "radeon"
    3. Intel cards typically use "intel"
  3. Device Identifiers for SMSC devices should be numbered sequentially, as in the examples below ("SMSCCard0", "SMSCCard1", etc.)
  4. It is very important to give the correct USB address in the 'Option "Device"' line. Plug all SMSC devices into the system, then use the command lssmsc in the terminal to show the USB addresses of all recognized SMSC devices.
  5. Use "GfxPort=HDMI" to use the HDMI output of the SMSC device, if applicable.
2. Section "Screen"
  1. Again, there must be one "Screen" section for each GPU/monitor.
  2. For the "Device" line, use the "Device" identifiers specified in the "Device" section.
  3. For simplicity, use Screen Identifiers that relate to the Device Identifiers. For example, "SMSCScreen0" using "SMSCCard0".
3. Section "ServerLayout"
  1. This section specifies the spatial relationship of the previously identified screens. Please see the examples below for extended and cloned server layout sections.
  2. Be sure to include the Options "Xinerama" "on" and "IgnoreABI" "True".

##### Extended ServerLayout xorg.conf file with 3 SMSC devices

Section "Files"
        ModulePath "/usr/lib/nvidia-current"
        ModulePath "/usr/local/lib/xorg/modules"
        ModulePath "/usr/lib/xorg/modules"
        ModulePath "/usr/lib64/xorg/modules"
        ModulePath "/usr/lib/userful/xorg/modules"
EndSection

Section "Device"
        Identifier "OnboardCard"
        Driver "radeon"
        VendorName "ATI"
        BoardName "ATI card"
EndSection

Section "Device"
        Identifier "SMSCCard0"
        Driver "smsc"
        Option "Device" "usb-0000:00:12.2-2.1"
        Option "SGFX" "GfxPort=VGA"
EndSection

Section "Device"
        Identifier "SMSCCard1"
        Driver "smsc"
        Option "Device" "usb-0000:00:13.2-3.1"
        Option "SGFX" "GfxPort=VGA"
EndSection

Section "Device"
        Identifier "SMSCCard2"
        Driver "smsc"
        Option "Device" "usb-0000:00:13.2-4.1"
        Option "SGFX" "GfxPort=VGA"
EndSection

Section "Screen"
        Identifier "OnboardScreen"
        Device "OnboardCard"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "Screen"
        Identifier "SMSCScreen0"
        Device "SMSCCard0"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "Screen"
        Identifier "SMSCScreen1"
        Device "SMSCCard1"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "Screen"
        Identifier "SMSCScreen2"
        Device "SMSCCard2"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "ServerLayout"
    Identifier "Extended"
    Screen 0 "OnboardScreen"
    Screen 1 "SMSCScreen0" RightOf "OnboardScreen"
    Screen 2 "SMSCScreen1" RightOf "SMSCScreen0"
    Screen 3 "SMSCScreen2" RightOf "SMSCScreen1"
    Option "Xinerama" "on"
    Option "IgnoreABI" "True"
EndSection

##### Cloned ServerLayout xorg.conf file with 3 SMSC devices

Section "Files"
        ModulePath "/usr/lib/nvidia-current"
        ModulePath "/usr/local/lib/xorg/modules"
        ModulePath "/usr/lib/xorg/modules"
        ModulePath "/usr/lib64/xorg/modules"
        ModulePath "/usr/lib/userful/xorg/modules"
EndSection

Section "Device"
        Identifier "OnboardCard"
        Driver "intel"
        VendorName "Intel"
        BoardName "Intel card"
EndSection

Section "Device"
        Identifier "SMSCCard0"
        Driver "smsc"
        Option "Device" "usb-0000:00:1d.0-1.1.1"
        Option "SGFX" "GfxPort=VGA"
EndSection

Section "Device"
        Identifier "SMSCCard1"
        Driver "smsc"
        Option "Device" "usb-0000:00:1d.0-1.2.1"
        Option "SGFX" "GfxPort=VGA"
EndSection

Section "Device"
        Identifier "SMSCCard2"
        Driver "smsc"
        Option "Device" "usb-0000:00:1d.0-1.4.1"
        Option "SGFX" "GfxPort=VGA"
EndSection

Section "Screen"
        Identifier "OnboardScreen"
        Device "OnboardCard"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "Screen"
        Identifier "SMSCScreen0"
        Device "SMSCCard0"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "Screen"
        Identifier "SMSCScreen1"
        Device "SMSCCard1"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "Screen"
        Identifier "SMSCScreen2"
        Device "SMSCCard2"
        Monitor "Monitor0"
        DefaultDepth 24
        SubSection "Display"
        Depth 16
        EndSubSection
        SubSection "Display"
        Depth 24
        EndSubSection
EndSection

Section "ServerLayout"
    Identifier "Cloned"
    Screen 0 "OnboardScreen"
    Screen 1 "SMSCScreen0"
    Screen 2 "SMSCScreen1"
    Screen 3 "SMSCScreen2"
    Option "Xinerama" "on"
    Option "IgnoreABI" "True"
EndSection

### With Userful MultiSeat
With Userful MultiSeat™, display configuration is managed through the Userful Control Center™. The Viewspan application cannot be used when Userful MultiSeat is activated due to a conflict between the Xinerama (used by Viewspan) and XRandR (used by Userful MultiSeat) X server extensions.
# USB Hotplugging
The SMSC-Driver supports hotplugging. The UFX device can be physically unplugged from the system without returning the system to a single-screen configuration. Simply re-plug the device to resume the active session.
If using the SMSC Viewspan application with the driver for a stand-alone extended or mirrored desktop configuration, please note that the ViewSpan application will launch whenever a UFX device is plugged in. To resume the session without changing monitor configuration, click "Cancel" on the ViewSpan panel to close it without changing the configuration file.
If more than one SMSC device is plugged into a system, the Viewspan application will choose the first one to be enumerated as the active, configurable device.

# Summary of Known Issues and Limitations
### Mouse Pointer Issues on Cloned Desktop in Mirrored Mode
In Mirrored Desktop Mode, the mouse pointer is visible only on the primary monitor. This appears to be a Xinerama/X issue that is independent of the SMSC-Driver for Linux. On occasion, a user will be able to move the mouse pointer to the cloned monitor(s) and be unable to move it back to the primary monitor. Should this occur, log out of the user session and log back in to reset X.
### “Two-Layer” Desktop Background Effect on One Monitor when Aspect Ratios Clash
If the aspect ratios of the monitors used in cloned desktop mode differ, the larger monitors may appear to have a smaller desktop background overlaying a larger background. This is due to the way that the Xinerama extension calculates screen sizes. To avoid this issue, use two monitors of the same size and native resolution(s), or at least the same aspect ratio.
### Gnome Panel Not Visible on Primary Monitor
If monitors with different aspect ratios and/or significantly different sizes or native resolutions are used in extended mode, the top and/or bottom Gnome Panel may not be visible on the primary monitor. This is due to a Xinerama issue where the wrong monitor is chosen as the limiting factor in resolution.
### Mouse Pointer Duplicated On Screen Border When Moved Between Monitors in Extended Mode
If monitors with different aspect ratios and/or significantly different sizes or native resolutions are used in extended mode, the mouse pointer may appear on two monitors if moved to the edge of one screen. This is due to a Xinerama issue where the wrong monitor is chosen as the limiting factor in resolution.
### Full-Screen Video Borders Corrupted In Mirrored Mode
If monitors with different aspect ratios and/or significantly different sizes or native resolutions are used in mirrored mode, the borders of full-screen video may appear corrupted. This is due to a Xinerama issue where the wrong monitor is chosen as the limiting factor in resolution.
Application refresh rate slows when using multiple video devices.
When manually configuring the xorg.conf file to support multiple SMSC UFX devices in single X Server using extended or cloned modes, the application refresh rate slows down with each additional device used. This is most easily observed when dragging a web browser across monitor boundaries. When dragging stops the application will refresh correctly. This issue is independent of the SMSC Linux driver and is due to a known Xinerama scaling problem which causes each application to redraw itself for each configured screen regardless if the application is visible on that screen. To avoid this, keep the number of video devices for each X Server low, use a high performance machine, or if possible run each device in a separate X Server.

Release History
Version - v1.0.2.1_20111206 (December 06, 2011)
Updated Vid Pid list of the supported devices.